## Slide 1: Clownfish Instruction Fetch Unit Arch review
Version 0.0.1
Shawn.Tan

## Slide 2: Outlines
IFU Architecture Overview
Program Counter Generator
Simple Branch Predictor Unit
Address Manager
Mini Decoder
ICCM and IBU

## Slide 3: IFU Architecture Overview
Design Specification:
Fetch one instruction every cycle without bubble
Fetch Ultra-Width instructions to hide latency and cache the leftover instructions
Support RV32I/RV32C (XLEN == 16bit or 32bit)
Support ICCM with multi bank(odd-even interleaving, Data Width 128bit)
Support Instruction Bus access(Data Width 128bit)
3-stage pipeline and unidirectional back pressure chain from Memory
Support LeftOver Buffer for RV32I/RV32C hybrid program
Support Static Branch Predictor with Back Taken Forward Not Taken(BTFN)
Support Return Address Stack(RAS) for Function in/out
Support mini Instruction Decoder for predicting jump/function stack push/pop

## Slide 4: IFU Architecture Overview
Fig1.1 Clownfish v0.0.1 IFU overall architecture

## Slide 5: IFU Architecture Overview
Arch Summary:
IFU was the frontend of CPU to fetch instruction from memory. It will be required to get utral-width data per cycle to prevent pipeline bubble, Especially in SuperScalar design. Our design will fetch 4-8 instructions and send only one every cycle. The leftover data will be cached in buffer for next cycles.
Once power up or reset release, PC generator got the first PC value from OTP/Effuse and worked at Machine Mode, which permitted to access all the region of system. The PC value would be executed address decoding by Address Manager and was sent to memory or BUS for read. The latency from memory or IBU will make Address manager and PC generator enter HOLD State by back pressure to prevent instruction loss. In the HOLD state, these module would keep its before output. The relationship of back pressure r must be a unidirectional chain not a ring to prevent deadlock. the back pressure must only be permitted from ICCM/IBU or IR.
The data from memory or IBU will be decoding by mini decoder. Firstly, the 128bit data would be split to 8 16bit parts and distinguish the instruction type of each parts. Generally, a 128bits data would contain 4-8 instructions. Next, the Instruction Router would assemble all the parts to whole RV32I/RV32C instructions by types. For Example, if a part is the low 16bit part of a RV32I instruction, it will be spliced with its next closed 16bit parts to a whole instruction, if the part type was RV32C, it was a whole RV32C instructions by itself. All the instructions will be decoding parallelly, and then the first instruction will be sent to IR directly and others will be cached in buffer. The PC generator and Address manager will at IDLE state until all the cached instructions sent out.

## Slide 6: IFU Architecture Overview
The Instruction Request Controller undertook the buffer pointer calculating and new Instr-Fetch request issuing to PC Gen . Our design had 3-stage pipeline and need at least 3cycles to obtain a data after new Instr-Fetch request sent. If we only fetch 32bit data every cycle, it means that the current instruction in sending state could not affect its next closed one when the pipeline is full. We use ultra-width fetch to solve this problem, hiding latency in routine from PC generator to memory. Every cycle, we will fetch 128bit data with little-endian and split it to each instructions. We would obsolete these instructions which was at the back of the first “jump” instruction in current data. The left will be sent one by one , and the InstrReqController would send new instr-fetch request two cycles before the jump instruction turns. So that just the jump instruction was sent, the new 128 bit data can be input to mini-decoder without pipeline bubbles. If there was no jump instructions in data, all the instructions would be sent, and InstrReqController would send new instr-fetch request two cycle before the last one.
there was still three cases that we could not hide its latency:
1. EU flush occurred, all the pipeline would be flushed and regain the new instructions. there
was 2 cycles not be hidden.
2. The first instruction in current data is jump case, it means the other instructions would be discard,
and the new instr-fetch operation will launched immediately. There were 2 cycles not be hidden. and
it’s the worst case.
3. The second instruction is jump, there would be 1 cycle lost .

## Slide 7: IFU Architecture Overview
A simple decoder was necessary to pre-recognize the direct jump (jal/jalr), conditional jump (bne, …….) , and function pop/push operation for BPU. We implemented RAS pool(a LIFO to store the return address of function) and BTFN logic in static BPU to optimize the procedure of function in/out and program cyclic structure.
The ICCM was a multi-banks SRAM with odd-even interleaving to adapt RV32C/RV32I hybrid code. By the help of LeftOver Buffer, we would store the 127bit-120bit of data when it was the low half of a RV32I instruction which can’t be sent. If LeftOver Buffer not empty, the InstrReqController will launch new instr-fetch operation 2 cycles before the last whole instruction sent. So that the new 128 bits would bring the other half of the leftover. and make up a whole instruction with the Buffer content.

## Slide 8: Program Counter Generator
Fig2.1 Clownfish v0.0.1 PC Generator FSM Flow

## Slide 9: Simple Branch Predictor Unit

## Slide 10: Address Manager
Fig2.1 Clownfish v0.0.1 address Manager FSM Flow

## Slide 11: Mini Decoder

## Slide 12: Simple Branch Predictor Unit

## Slide 13: Program Counter Generator

## Slide 14: ITCM

## Slide 15: IBU

## Slide 16: List of abbreviation